## Slide 1
OPTIFINERS
INDUSTRIAL ENGINEERING & MANAGEMENT

## Slide 2
Outline of Tentative Steps
OptiProductio: Smart Production Workflow and Resource Optimization System
Phase I
29 Oct 2026
• Pick and define the problem
• Literature review
• SMART objectives (PO1 to PO4)
• Design the 3-station line and parts list
• Plan the method and timeline
Phase II
__ / __ / 2026
• Wire sensors to Arduino UNO
• Python logger and dashboard
• Check counts against a hand tally
• First runs and partial results
• Dashboard on Bosch public data
Phase III
__ / __ / 2027
• Rebalance and WIP-limit experiments
• Results and discussion
• Live prototype demo
• Report, poster and PPT
• IEEE-format paper draft
Status today: Phase I planning done. Hardware build in progress. Red blanks = dates not announced yet.

## Slide 3
EL Phase-I
Presentation Outline
Introduction
Literature Review
Problem Definition
Objectives
Methodology and System Pipeline
Measurement Parameters
Research Process
Proposed Outcomes
Timeline of the Project
Conclusion
References
Expected Outcome by the End of First Year

## Slide 4
OVERVIEW OF THE TOPIC:
OptiProductio: a low-cost system that watches a small production line in real time and shows how well it is working.
How: sensors on a 3-station model line send every event (part done, part rejected, line stopped) to an Arduino UNO, which passes it to a Python dashboard on a laptop.
Why: small factories often record output by hand, so delays, pile-ups and the slowest station stay hidden until the end of the shift [2], [4].
What it adds: an alert when too many parts pile up inside the line (a WIP limit), based on the CONWIP idea [5].
INTRODUCTION
Production count
IR sensor at each station exit
Cycle time
time each station takes per part
Inventory
raw material bin level and WIP
Workflow
bottleneck, stops and pile-ups
EL topic: Smart Production Workflow and Resource Optimization System. Deliverable: production efficiency dashboard.

## Slide 5
Literature Review
Key studies and findings
Study | What they did | Key finding
Hwang et al., 2017 [2] | IoT performance-measurement model built on the ISA-95 and ISO 22400 standards | IoT timestamp data can give OEE numbers in real time
Ng Corrales et al., 2020 [3] | Systematic review of OEE: 862 articles screened down to 186 | Many industries adapt OEE, because the basic formula alone is not enough
Wicaksono et al., 2024 [4] | Replaced manual OEE logging with an ESP32 board over MQTT | Works in real time, but reports up to 16% OEE error
Spearman et al., 1990 [5] | Proposed CONWIP: a fixed cap on the total parts inside a line | A simple pull alternative to kanban that limits WIP
Thürer et al., 2023 [6] | Tested kanban, CONWIP and a hybrid on a physical lab-scale line | WIP limits cut the time a job spends in the line but can lower throughput

## Slide 6
Trends in literature: low-cost IoT boards now give real-time OEE [2], [4]; WIP limits like CONWIP are mostly tested in simulation or lab models [6], [9]; public line data such as the Bosch dataset is used mainly to predict failed parts [8].
Theoretical framework:
  Little's law: average WIP = throughput × average flow time [7]. Cut WIP at the same throughput and parts spend less time in the line.
  OEE = Availability × Performance × Quality [3], [10].
  CONWIP: release a new part only when a finished part leaves [5].
Relevance to our project: monitoring papers report numbers but do not control the flow, and WIP-limit papers control the flow but are rarely tied to a live, measured line [6], [9]. Low-cost builds rarely check their accuracy against a manual count [4]. OptiProductio does all three on one small line.
Literature Review (contd.)

## Slide 7
Clear statement of the problem: small production units cannot see count, cycle time, inventory and WIP while the line is running, so they find bottlenecks and pile-ups too late to act.
Context of the problem: MSMEs gave 30.1% of India's GDP (2022-23) and 45.73% of its exports (2023-24) [1]. Manual OEE recording is slow because operators write data at the machine and supervisors process it later [4]. Ordinary performance systems struggle to capture what is actually happening on the floor in real time [2].
Significance of addressing it: if work is released without a limit, WIP between stations can keep growing [11], parts wait longer, and the slowest station stays hidden.
Gap and novelty: low-cost monitoring and WIP control are studied separately [4], [9]. OptiProductio puts both on one prototype costing under ₹2,000 (our estimate), and checks its own counts against a hand tally and Little's law [7].
Problem Definition

## Slide 8
Main objective: build a low-cost hardware and software prototype that measures production count, cycle time, inventory and WIP on a 3-station model line in real time, and use it to find the bottleneck and test a WIP limit.
Objectives
PO | Specific objective | Measurable target | By
PO1 | Count parts at all 3 stations with IR sensors | Count error ≤ 2% against a hand tally, over three 10-minute runs | Phase II
PO2 | Live dashboard: count, cycle time per station, WIP, bin level, downtime, OEE proxy | Refreshes every 2 s or faster; all 6 numbers on one screen | Phase II
PO3 | Find the bottleneck and rebalance the line | Report throughput and flow time before and after, 3 runs each; Little's law gap ≤ 10% | Phase III
PO4 | WIP-limit alert (LED, buzzer, dashboard) | Alert fires at the cap every time; trade-off reported for caps 2, 4, 6 | Phase III
Why achievable: parts are standard IDEA Lab kit, the code is already written and tested on sample data, and each PO is checked by a simple count or timer. Expected contribution: a cheap, open template for monitoring and WIP control that small units and student labs can copy.

## Slide 9
Design: quantitative and experimental. Build the line, measure it, change one thing at a time (rebalance, then WIP limit) and compare the numbers.
Data collection: IR sensors time every part leaving each station; buttons log breakdown, no-material and reject; an ultrasonic sensor reads the raw material bin. The Arduino stamps each event in milliseconds and sends it over USB to a Python logger (CSV). Secondary data: the public Bosch production line dataset [8], [12].
Data analysis: throughput, cycle time per station, WIP and flow time from the event log; Little's law as a cross-check [7]; OEE proxy = A × P × Q [3]; mean and spread across 3 repeat runs.
Tools: Arduino IDE (C++), Python (pyserial, pandas, Streamlit), Excel for result tables.
Risks and fallbacks: miscounts (cardboard gates, debounce, hand tally check); hardware failure on demo day (replay a saved run); Bosch time units are not published (use only for relative comparison).
Methodology

## Slide 10
System Pipeline
Raw material bin
ultrasonic sensor
Station 1: Cut
IR sensor D2
Station 2: Drill
IR sensor D3 (slow on purpose)
Station 3: Inspect
IR D4 + Reject button
Physical line (parts moved by hand)
Control panel
Breakdown, No-material buttons
Arduino UNO
timestamps every event
Andon on the line
LCD, red/green LED, buzzer
Python logger
USB serial to CSV event log
Bosch public dataset
converted to the same events
Metrics engine
count, cycle time, WIP, OEE
Streamlit dashboard
live KPIs and WIP alert
WIP cap sent back to Arduino

## Slide 11
Measurement Parameters
No machine-learning model is trained in this project. These are the measurement settings we will report.
Item | Value
Data sources | Live line event log (CSV) and a Bosch sample: first 50,000 rows, line L3, 3 busiest stations [12]
Event format | time (s), event (PASS / SCRAP / DOWN / UP), station, reason
Sensor timing | IR debounce 400 ms; button debounce 200 ms; status sent every 1 s; dashboard refresh 2 s
Cycle time (per station) | finish(k) − max(arrive(k), finish(k−1)), so stations after the bottleneck do not look slow
WIP | parts released at Station 1 minus parts that left Station 3 (good or scrap)
Throughput / flow time | good parts per minute / exit time − entry time per part; checked with Little's law [7]
OEE proxy | A × P × Q [3]; ideal cycle time set by the team: __ s
Experiments | baseline, rebalanced, WIP cap 2 / 4 / 6; 10 minutes per run, 3 repeats each
Targets | count error ≤ 2%; Little's law gap ≤ 10%; alert fires every time WIP reaches the cap

## Slide 12
Research Process
Literature review
Define problem and POs
Design line and parts list
Build and wire
Calibrate: count vs hand tally
Error ≤ 2%?
No: adjust
Fix gates and sensor range
Yes
Run 1: baseline
Find bottleneck
Run 2: rebalanced
Run 3: WIP caps 2/4/6
Analyse: Little's law, OEE
Repeat on Bosch public data
Report, poster, paper draft

## Slide 13
Expected results: a working prototype (3-station line and live dashboard) and a results table comparing baseline, rebalanced and WIP-capped runs: throughput, average WIP, flow time, cycle time per station, OEE proxy and scrap rate.
Success criteria: PO1 to PO4 met. Improvement after rebalancing: __ % (to be measured, not assumed).
Potential impact: shows that count, cycle time, inventory and workflow can be watched live with low-cost parts, as a template for small units and student labs.
Limits we will state: OEE is a proxy (our own ideal cycle time); parts are moved by hand; Bosch time units are estimated by the Kaggle community, not published by Bosch [8].
Future research directions: wireless boards, more stations and product types, and testing the WIP-limit alert on more real factory data.
Proposed Outcomes

## Slide 14
Timeline of the Project
Sprint | Dates | Work | Linked to | Status
1 | 23 to 29 Oct 2026 | Problem, literature review, POs, line design, parts list, code skeleton | Phase I review (29 Oct) | Done
2 | 30 Oct to 1 Nov 2026 | Wire all sensors, logger and dashboard running together | PO1, PO2 | In progress
3 | 2 Nov to __ | Count accuracy test, Bosch data mode, first runs | PO1, PO2, Phase II | Not started
4 | __ to __ | Baseline, rebalance and WIP-cap experiments (3 repeats each) | PO3, PO4 | Not started
5 | __ to __ | Results, report, poster, PPT, paper draft, demo rehearsal | Phase III | Not started
Phase II date: __ / __ / 2026 Phase III date: __ / __ / 2027 (dates to be announced; sprints will be fixed backwards from them)

## Slide 15
Summary of key points: OptiProductio measures production count, cycle time, inventory and workflow on a 3-station model line, live, using an Arduino UNO, low-cost sensors and a Python dashboard.
What makes it different: it adds a WIP-limit alert based on CONWIP [5], and it checks its own numbers against a hand tally and Little's law [7].
Final thought: you cannot improve a line you cannot see. OptiProductio makes the line visible cheaply.
Next steps: finish wiring by 1 Nov, run the count accuracy test (PO1), then bring partial results to Phase II.
Conclusion

## Slide 16
[1] Press Information Bureau. (2024, December 23). The MSME revolution: Transforming India's economic landscape. Government of India. https://static.pib.gov.in/WriteReadData/specificdocs/documents/2024/dec/doc20241223476301.pdf
[2] Hwang, G., Lee, J., Park, J., & Chang, T.-W. (2017). Developing performance measurement system for Internet of Things and smart factory environment. International Journal of Production Research, 55(9), 2590–2602. https://doi.org/10.1080/00207543.2016.1245883
[3] Ng Corrales, L. del C., Lambán, M. P., Hernandez Korner, M. E., & Royo, J. (2020). Overall equipment effectiveness: Systematic literature review and overview of different approaches. Applied Sciences, 10(18), 6469. https://doi.org/10.3390/app10186469
[4] Wicaksono, A. A., Ningsih, Y. K., & Surjati, I. (2024). Implementation of MQTT protocol on ESP32-based OEE analysis development board. Emitor: Jurnal Teknik Elektro, 24(2), 169–175. https://doi.org/10.23917/emitor.v24i2.3908
[5] Spearman, M. L., Woodruff, D. L., & Hopp, W. J. (1990). CONWIP: A pull alternative to kanban. International Journal of Production Research, 28(5), 879–894. https://doi.org/10.1080/00207549008942761
[6] Thürer, M., Li, S. S., Yang, C., Qu, T., & Huang, G. Q. (2023). Does regulating work-in-process increase throughput and reduce cycle times? An assessment by lab scale system models. In Advances in Production Management Systems (APMS 2023), IFIP AICT 691 (pp. 649–661). Springer. https://doi.org/10.1007/978-3-031-43670-3_45
[7] Little, J. D. C. (2011). Little's law as viewed on its 50th anniversary. Operations Research, 59(3), 536–549. https://doi.org/10.1287/opre.1110.0940
References

## Slide 17
[8] Mangal, A., & Kumar, N. (2017). Using big data to enhance the Bosch production line performance: A Kaggle challenge. arXiv. https://arxiv.org/abs/1701.00705
[9] Pettersen, J.-A., & Segerstedt, A. (2009). Restricted work-in-process: A study of differences between Kanban and CONWIP. International Journal of Production Economics, 118(1), 199–207.
[10] International Organization for Standardization. (2014). Automation systems and integration: Key performance indicators (KPIs) for manufacturing operations management. Part 2 (ISO 22400-2:2014). https://www.iso.org/standard/54497.html
[11] Cordon, C. (1995). Quality defaults and work-in-process inventory. European Journal of Operational Research, 80(2), 240–251.
[12] Bosch. (2016). Bosch production line performance [Data set]. Kaggle. https://www.kaggle.com/c/bosch-production-line-performance
[13] The Patents Act, 1970, § 3(k) (India). https://www.indiacode.nic.in/handle/123456789/1392
References (contd.)

## Slide 18
Product prototype: a working OptiProductio line and dashboard, released as open source (code, wiring table and build guide) so other labs can rebuild it.
Conference publication: a short paper in IEEE format on the prototype, the accuracy check and the WIP-limit experiments. Target venue to be chosen once results are in.
Research proposal: extend the work to more stations, wireless boards and more real factory data.
Patent: not planned. Software and algorithms on their own are generally not patentable in India (Patents Act, 1970, Section 3(k)) [13], so we will not claim one.
Expected Outcome by the End of First Year